DO NOT use the BBQ unless you have been instructed in its safe use and operation. Students must be supervised at all times.

### Do not leave the BBQ unattended once it is alight. Do not move the BBQ while 
it is in use. Do not store the BBQ until it has completely cooled after use.

### PRE-OPERATIONAL SAFETY CHECKS

- Before you start, check that hoses, connections, burner positions, igniter button, the fat drainage container and utensils are clean and in good repair.

- A regulator must be fitted to the gas supply line between the bottle and the BBQ.

- Use safe manual handling techniques to avoid muscle strain when transporting the BBQ. Get help, use ramps and trolleys to avoid any injury or damage.

- Set up the BBQ on flat ground that is away from any buildings, fences, trees or over-hanging shrubs.

- Never light a barbecue indoors or in a garage.

- Make sure the weather conditions are suitable for the BBQ activity. If it's windy, ensure the wind is blowing away from you when you light the barbecue.

- Keep children not involved in the BBQ activity away from the barbecue area.

- Don't wear loose clothing, or anything could dangle onto the flames.

- Keep fire extinguisher handy in case of emergencies.

- Never leave the barbecue unattended and don't try to move it whilst it's lit.

#### OPERATIONAL SAFETY CHECKS

- Ensure the BBQ burner knobs are in the off position prior to use or any connections.

- Connect the BBQ regulator into the gas bottle by screwing it to the left, turn the gas bottle on slightly as it will be quicker to turn off in an emergency.

- Check all cylinder connections and hoses for leaks. Never use a match or lighter to check for leaks. Brush a mixture of 50% soap and 50% water onto all connections and hoses. Rising bubbles indicate a leak. Repair or tighten all connections until there are no bubbles.

- If there is no igniter button, insert the flame from a long match or barbecue lighter through the side burner hole, if you are using a match, light the match before you turn on the gas at the grill controls.

- If the burner doesn’t ignite, turn the gas off and wait five minutes before trying again.

#### Lighting instructions

- INSERT MANUFACTURER’S LIGHTING INSTRUCTIONS HERE.

#### HOUSEKEEPING

- Turn the gas bottle tap to close/off position in the direction of the arrow on the gas bottle.

- Turn the BBQ burner knobs to the OFF position.

- Disconnect/ unscrew the regulator from the gas bottle.

- Do not move the BBQ until it has cooled sufficiently to do so safely.

- Clean and store the BBQ and gas bottle safely and securely away.

## POTENTIAL HAZARDS

( Strains			( Burns (heat or fat)			( Fire			( Explosion          ( Gas inhalation

This SOP should be used in conjunction with

| Date of last review | ______________ | Signature ______________________ |
| --- | --- | --- |

# Text boxes

PORTABLE BBQ USE