DO NOT use this machine unless a teacher has instructed

you in its safe use and operation and has given permission.

| Safety glasses must be worn at all times in work areas. | Long and loose hair must be contained. |
| --- | --- |
| Appropriate footwear with substantial uppers must be worn. | Close fitting/protective clothing must be worn. |
| Rings and jewellery must not be worn. | Hearing protection must be worn when using this machine. |

### PRE-OPERATIONAL SAFETY CHECKS

- Ensure no slip/trip hazards are present in workspaces and walkways.

- Locate and ensure you are familiar with the operation of the ON/OFF starter and E-Stop (if fitted).

- Ensure the material is tightly clamped in the work vice.

- Check coolant delivery system to allow for sufficient flow of coolant.

- Faulty equipment must not be used. Report suspect machinery immediately.

#### OPERATIONAL SAFETY CHECKS

- Ensure that the work piece is secure.

- Support overhanging work and signpost if it presents a hazard.

- Ensure no-stands in front of the saw when it is started.

- Keep clear of moving machine parts.

- Direct coolant onto blade before starting cut.

- Never leave the machine running unattended.

- Before making adjustments or before cleaning swarf accumulations switch off and bring the machine to a complete standstill.

#### HOUSEKEEPING

- Switch off machine.

- Leave the machine and work area in a safe, clean and tidy state.

## POTENTIAL HAZARDS

##### (	Reciprocating saw arm

##### Metal splinters

##### (	Sharp edges and burrs

##### (	Loose clothing entanglement

##### (	Eye injuries

## FORBIDDEN

  - Attempting to cut very small items

  - Attempting to cut material other than metal

| Date of last review | ______________ | Signature ______________________ |
| --- | --- | --- |

# Text boxes

POWER HACKSAW – METAL